## Slide 1: Individual Homework
Exercise 5.1 – Boolean functions
Astăluș adrian claudiu

## Slide 2
Exercise 5.1 - Using Quine’s method, simplify the following Boolean functions given by their values 0.
f1(0,1,0) = f1(0,1,1) = f1(1,0,1) = 0
f1 is a Boolean function of 3 variables: f1: (B2)n → B2
When using the Quine – McClusky’s method, there are (quite) a few steps to follow:

## Slide 4
Solving the exercise
f1(0, 1, 0) = f1(0, 1, 1) = f1(1, 0, 1) = 0
⇒ f1(x1, x2, x3) = v x3 v x1 v x1x2 v x1x2x3
⇒ f1(x1, x2, x3) = m0 v m1 v m4 v m6 v m7
Knowing the values 0 of the function, we can determine the DCF of the function
° A DCF (disjunctive canonical form) is a disjunction of monoms
(minterms in our case)
° A monom is a conjunction of variable (in our case, x1, x2 and x3)
x1 | x2 | x3 | F1(x1, x2, x3)
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
From here, we can write the support set of f, as follows:
Sf = { (0, 0, 0), (0, 0, 1), (1, 0, 0), (1, 1, 0), (1, 1, 1) }
The support set is ordered in ascending order with respect to the number of “1” values in each triple
- the support set of f -

## Slide 5
Based on the support set of f, we make groups of minterms (delimited by horizontal lines), such that all the minterms belonging to the same group have the same number of values 1 as powers of variables. A double horizontal line marks the end of the representation of our initial function.
Therefore, from our support set of f1, we can determine 4 such groups:
- Group I, having the minterm (0, 0, 0) – m0
- Group II, having the minterms (1, 0, 0) and (0, 0, 1) – m4 and m1
- Group III, having the minterm (1, 1, 0) – m6
- Group IV, having the minterm (1, 1, 1) – m7
We take each neighboring groups ( I and II, II and III, III and IV) and apply the simple factorization. The result of the factorization of two neighbor monoms is a new monom represented as a row at the end of the tableau. The row contains the same values (0, 1 or -) in the columns corresponding to the common variables, where the symbol “-” is used when the variable is eliminated. The rows corresponding to the ‘factorized’ monoms are marked on the left side, meaning that they are not maximal monoms.

## Slide 6
Group | x1 | x2 | x3 | 
I | 0 | 0 | 0 | m0 ✓
II | 1 | 0 | 0 | m4 ✓
 | 0 | 0 | 1 | m1 ✓
III | 1 | 1 | 0 | m6 ✓
IV | 1 | 1 | 1 | m7 ✓
V = I + II | - | 0 | 0 | m0 v m4 = = max1
 | 0 | 0 | - | m0 v m1 = = max2
VI = II + III | 1 | - | 0 | m4 v m6 = x1 = max3
VII = III + IV | 1 | 1 | - | m6 v m7 = x1x2 = max4
Group | x1 | x2 | x3 | 
I | 0 | 0 | 0 | m0 ✓
II | 1 | 0 | 0 | m4 ✓
 | 0 | 0 | 1 | m1 ✓
III | 1 | 1 | 0 | m6 ✓
IV | 1 | 1 | 1 | m7 ✓
V = I + II | - | 0 | 0 | 
 | 0 | 0 | - | 
VI = II + III | 1 | - | 0 | 
VII = III + IV | 1 | 1 | - | m6 v m7 = x1x2 = max4
For the groups V, VI and VII we use the simple factorization
m1 and m6 cannot be factorized because they are not neighbors ( they differ by more than 1 variable)
We cannot apply double factorization because there are no two neighboring monoms ( from groups V and VI or VI and VII) that have a ‘-’ on the same column
The last 4 monoms are not checked, so they form the set of maximal monoms of f
M(f) = { max1, max2, max3, max4} – the set of maximal monoms of f1

## Slide 7
For obtaining the central monoms we use a new tableau representing the correspondence between the maximal monoms (on columns) and the minterms from the function’s expression (on rows).
A cell in the tableau is marked with a star (*) if the minterm corresponding to the row was used in factorization to obtain the maximal monom from the column.
A maximal monom is a central monom if there is a * on its column that is unique in its row.
The disjunction of all central monoms belongs to all simplified forms of the initial function.
 | max1 | max2 | max3 | max4 | 
m0 | ★ | ★ |  |  | - m0 covered by max1 and max2
m1 |  | ⍟ |  |  | - m1 covered by max2
m4 | ★ |  | ★ |  | - m4 covered by max1 and max3
m6 |  |  | ★ | ★ | - m6 covered by max3 and max4
m7 |  |  |  | ⍟ | - m7 covered by max4

## Slide 8
Because m1 and m7 are covered by only one maximal monom each, these two maximal monoms will be the central monoms
C(f) = { max2, max4 } – the set of central monoms of f1
M(f) ≠ C(f) ≠ 0 ⇒ we use the 2nd simplification case
g = max2 v max4
g covers m0, m1, m6 and m7 ⇒ f1S = g v max1 = v x1x2 v
f2S = g v max3 = v x1x2 v x1
m4 is not covered by g, so our final functions consist of g and a maximal monom that covers m4 (in this case, either max1 or max3)
 | max1 | max2 | max3 | max4 | 
m0 | ★ | ★ |  |  | - m0 covered by max1 and max2
m1 |  | ⍟ |  |  | - m1 covered by max2
m4 | ★ |  | ★ |  | - m4 covered by max1 and max3
m6 |  |  | ★ | ★ | - m6 covered by max3 and max4
m7 |  |  |  | ⍟ | - m7 covered by max4